## Slide 1
Lecture 1: Tiny Machine
The processor as an instruction interpreter
Notes: 1

## Slide 2
2
Outline
Von-Neumann Machine
Instruction Cycle
Fetch and Execute Cycle
Two Tiny Machines
  Accumulator Machine
  Load/Store Machine
Assembly Language
Notes: 2

## Slide 3
3
Instruction Cycle
In the von-Neumann machine, the Instruction Cycle (also Machine Cycle) is a loop that repeats the following two steps over and over again:
Fetch Cycle
Execute Cycle

## Slide 4
4
Fetch/Execution Cycle
Fetch Cycle: Instruction is retrieved from memory.
Execute Cycle: Instruction is executed.

## Slide 5
5
Hardware Description Language
We will use a simple Hardware Description Language to understand how instructions are fetched and executed in the VN.

## Slide 6
6
Accumulator Machine
PC
MAR
A
MDR
OP ADDRESS
MEMORY
A L U
Decoder
IR

## Slide 7
7
Definitions
Program Counter (PC) is a register that holds the address of the next instruction to be executed.
Memory Address Register (MAR) is a register used to store the address to a specific memory location in Main Storage so that data can be written to or read from that location.
Main Storage (MEM) is used to store programs and data. Random Access Memory (RAM) is a implementation of MEM.

## Slide 8
8
Definitions
Memory Data Register (MDR) is a register used to store data that is being sent to or received from the MEM. The data that it stores can either be in the form of instructions or simple data such as an integer.
Instruction Register (IR) is a register that stores the instruction to be executed by the processor.

## Slide 9
9
Definitions
Arithmetic Logic Unit (ALU) is used to execute mathematical instructions such as ADD or SUB.
Decoder is a circuit that decides which instruction the processor will execute. For example, it takes the instruction op-code from the IR as input and outputs a signal to the ALU to control the execution of the ADD instruction.
Accumulator (A) is used to store data to be used as input to the ALU.

## Slide 10
10
Fetch Cycle
The data flow for the Fetch Cycle consists of 4 steps.

## Slide 11
11
Data Movement 1
Given registers PC and MAR, the transfer of the contents of PC into MAR is indicated as:
MARPC
A
PC
MAR
MDR
OP ADDRESS
MEMORY
A L U
Decoder

## Slide 12
12
Data Movement 2
To transfer information from a memory location to the register MDR, we use:
MDRMEM[MAR]
The address of the memory location has been stored previously into the MAR register
PC
MAR
MDR
OP ADDRESS
MEMORY(MEM)
A L U
Decoder
A
MEM[MAR]

## Slide 13
13
Data Movement 3
We denote the transfer of MDR to IR by:
IRMDR
A
PC
MAR
MDR
OP ADDRESS
MEMORY
A L U
Decoder

## Slide 14
14
Instruction Register
The instruction register IR has two fields:
IR.OP operation
IR.ADDR address

## Slide 15
15
Instruction Format
The instruction format of the accumulator machine is:
OP
ADDR
01
0000 0000 0010

## Slide 16
16
Data Movement 4
DECODERIR.OP
PC
MAR
MDR
OP ADDRESS
MEMORY
A L U
Decoder
A

## Slide 17: Decoder
If DECODER == 00, then the decoder will perform the fetch cycle.
If DECODER != 00, then the decoder will perform the execution cycle.
The operation is determined by DECODER.

## Slide 18
18
00 Fetch Cycle
MAR  PC
MDR  MEM[ MAR ]
IR  MDR
PC  PC+1
DECODER  IR.OP

## Slide 19
19
01 LOAD
MAR  IR.ADDR
MDR  MEM[ MAR ]
A  MDR
DECODER  00

## Slide 20
20
02 ADD
MAR  IR.ADDR
MDR  MEM[ MAR ]
A  A + MDR
DECODER  00

## Slide 21
21
Data Movement
We denote the transfer of MDR to MEM at location by
MEM[ MAR ]  MDR

## Slide 22
22
03 STORE
MAR  IR.ADDR
MDR  A
MEM[ MAR ]  MDR
DECODER  00

## Slide 23
23
07 HALT

## Slide 24
24
Instruction Set Architecture (ISA)
00 - FETCH
Fetches instruction from memory (hidden instruction)

## Slide 25
25
Instruction Set Architecture
01 - LOAD <X>
Loads the contents of memory location “X” into A (A stands for Accumulator).
02 - ADD <X>
The data value stored at address “X” is added to A and the result is stored back in A.
03 - STORE <X>
Store the contents of A into memory location “X”.
04 - SUB <X>
The data value stored at address “X” is subtracted from A and the result is stored back in A.

## Slide 26
26
Instruction Set Architecture
05 - IN <Device #>
A value from the input device is transferred into A.
06 - OUT <Device #>
Print A to the output device.
Device # Device
5 Keyboard
7 Printer
9 Screen
For instance you can write: 003 IN <5> “23” where “23” is the value you are typing in.

## Slide 27
27
Instruction Set Architecture
07 - Halt
The machine stops execution of the program.
(Return to the OS)
08 - JMP <X>
Causes an unconditional branch to address “X”.
PC  X
09 - SKIPZ
If A equals 0 then PC  PC + 1 (the next instruction is skipped).
(If the output of the ALU equals zero, the Z flag is set to 1. In this machine we test the flag and if Z = 1 the next instruction is skipped (PC  PC + 1)

## Slide 28
28
MAR
A
MDR
OP ADDRESS
MEMORY
A L U
Decoder
PC
If the output of the ALU equals zero, the Z flag is set to 1
0
A = 0
Z
Z =Condition Code

## Slide 29
29
Instruction Set Architecture
For this tiny assembly language, we are
using only one condition code (CC) Z = 0 .
Condition codes indicate the result of the most
recent arithmetic operation
Two more flags (CC) can be incorporated to test negative and positives values:
G = 1 Positive value
Z = 1 Zero
L = 1 Negative value

## Slide 30
30
Program State Word (Condition Codes - CC)
PC
Interrupt Flags
MASK
Mode
OV
MP
PI
To be defined later
I/O
TI
SVC
CC
Z
G
L
The PSW is a register in the CPU that provides the OS with
information on the status of the running program

## Slide 31
31
Instruction Descriptions
opcode mnemonic meaning
0001 LOAD <x> A  MEM[x]
0010 ADD <x> A  A + MEM[x]
0011 STORE <x> MEM[x]  A
0100 SUB <x> A  A – MEM[x]
0101 IN <Device_#> A  Device
0110 OUT <Device_#> A  Device
0111 HALT Stop
1000 JMP <x> PC  x
1001 SKIPZ Z = 1 skip
1010 SKIPG G = 1 skip
1011 SKIPL L= 1 skip

## Slide 32
32
Assembly Language Programming Examples
Assign a memory location to each variable:
C  X + Y
<000> <001> <002>

## Slide 33
33
Assembly Language Programming Examples
Memory
000 1245
001 1755
002 0000
003 Load <000>
004 Add <001>
005 Store <002>
006 Halt
Memory
000 1245
001 1755
002 3000
003 Load <000>
004 Add <001>
005 Store <002>
006 Halt
After execution

## Slide 34
34
Assembler: translate symbolic code to executable code (binary)
Assembly Language
003 Load <000>
004 Add <001>
005 Store <002>
006 Halt
003 0001 0000 0000 0000
004 0010 0000 0000 0001
005 0011 0000000000010
006 0111 0000000000000
In binary
01  LOAD 06  OUT
02  ADD 07  HALT
03  STORE 08  JMP
04  SUB 09  SKIPZ
05  IN
Assembler

## Slide 35
35
Assembler Directives
The next step to improve our assembly language is the incorporation of pseudo-ops (assembler directives) to invoke a special service from the assembler (pseudo-operations do not generate code)
.begin  tells the assembler where the program starts
.data  tells the assembler to reserve a memory location.
.end  tells the assembler where the program ends.
Labels are symbolic names used to identify memory
locations.

## Slide 36
36
Assembler Directives
This is an example of the usage of assembler directives
.begin
Assembly language instructions
halt return to OS
.data tells to reserve a memory location
.end tells the assembler where the program ends

## Slide 37
37
Assembly Language Programming Examples
Label opcode address
start .begin
in x005
store a
in x005
store b
load a
sub TWO
add b
out x009
halt
a .data 0
b .data 0
TWO .data 2
.end start
Data section
Text section (code)

## Slide 38
Load/Store Architecture
A load/store architecture has a “register file” in the CPU
and it uses three instruction formats. Therefore, its assembly
language is different from the one of the accumulator machine.
OP
OP
OP
ADDRESS
ADDRESS
Ri
R i
R j
R k
JMP <address>
Load R3, <address>
Add R3, R2, R1
Notes: 38

## Slide 39
39
Load/Store Architecture
PC
MAR
MDR
OP
MEMORY
A L U
Decoder
R0
R1
R2
R3
+
INPUT/OUT

## Slide 40
40
Multiplying two numbers
Label opcode address
start .begin
in x005
store a
in x005
store b
here load result
add a
store result
load b
sub ONE
store b
skipz
jmp here
load result
out x009
halt
a .data 0
b .data 0
ONE .data 1
result .data 0
.end start
One address Architecture
(six memory access inside the loop)
Label opcode address
start .begin
in x005
store R0, a
in x005
store R0, b
load R2, result
load R3, a
load R0, b
load R1, ONE
here add R2, R2, R3
sub R0, R0, R1
skipz
jmp here
store R2, result
load R0, result
out x009
halt
a .data 0
b .data 0
ONE .data 1
result .data 0
.end start
Load/Store architecture
(no memory access inside the loop)

## Slide 41
Lecture 2
Next time will talk about the PM/0 virtual machine
Notes: 41